## Slide 1: Chapter 2: Securing Network Devices
CCNA Security v2.0

## Slide 2: Chapter Outline
2.0 Introduction
2.1 Securing Device Access
2.2 Assigning Administrative Roles
2.3 Monitoring and Managing Devices
2.4 Using Automated Security Features
2.5 Securing the Control Plane
2.6 Summary

## Slide 3: Section 2.1: Securing Device Access
Upon completion of this section, you should be able to:
Explain how to secure a network perimeter.
Configure secure administrative access to Cisco routers.
Configure enhanced security for virtual logins.
Configure an SSH daemon for secure remote management.

## Slide 4: Topic 2.1.1: Securing the Edge Router

## Slide 5: Securing the Network Infrastructure
Notes: 2.1.1.1 Securing the Network Infrastructure

## Slide 6: Edge Router Security Approaches
Single Router Approach
Defense in Depth Approach
DMZ Approach
Notes: 2.1.1.2 Edge Router Security Approaches

## Slide 7: Three Areas of Router Security
Notes: 2.1.1.3 Three Areas of Router Security

## Slide 8: Secure Administrative Access
Tasks:
Restrict device accessibility
Log and account for all access
Authenticate access
Authorize actions
Present legal notification
Ensure the confidentiality of data
Notes: 2.1.1.4 Secure Administrative Access

## Slide 9: Secure Local and Remote Access
Local Access
Remote Access Using Telnet
Remote Access Using Modem and Aux Port
Notes: 2.1.1.5 Secure Local and Remote Access

## Slide 10: Secure Local and Remote Access (Cont.)
Dedicated Management Network
Notes: 2.1.1.5 Secure Local and Remote Access

## Slide 11: Topic 2.1.2: Configuring Secure Administrative Access

## Slide 12: Strong Passwords
Guidelines:
Use a password length of 10 or more characters.
Include a mix of uppercase and lowercase letters, numbers, symbols, and spaces.
Avoid passwords based on easily identifiable pieces of information.
Deliberately misspell a password (Smith = Smyth = 5mYth).
Change passwords often.
Do not write passwords down and leave them in obvious places.
Weak Password | Why it is Weak | Strong Password | Why it is Strong
secret | Simple dictionary password | b67n42d39c | Combines alphanumeric characters
smith | Mother’s maiden name | 12^h u4@1p7 | Combines alphanumeric characters, symbols, and includes a space
toyota | Make of car |  | 
bob1967 | Name and birthday of user |  | 
Blueleaf23 | Simple words and numbers |  | 
Notes: 2.1.2.1 Strong Passwords

## Slide 13: Increasing Access Security
Notes: 2.1.2.2 Increasing Access Security

## Slide 14: Secret Password Algorithms
Guidelines:
Configure all secret passwords using type 8 or type 9 passwords
Use the enable algorithm-type command syntax to enter an unencrypted password
Use the username name algorithm-type command to specify type 9 encryption
Notes: 2.1.2.3 Secret Password Algorithms

## Slide 15: Securing Line Access
Notes: 2.1.2.4 Securing Line Access
Syntax Checker: Secure Administrative Access on R2

## Slide 16: Topic 2.1.3: Configuring Enhanced Security for Virtual Logins

## Slide 17: Enhancing the Login Process
Virtual login security enhancements:
Implement delays between successive login attempts
Enable login shutdown if DoS attacks are suspected
Generate system-logging messages for login detection
Notes: 2.1.3.1 Enhancing the Login Process

## Slide 18: Configuring Login Enhancement Features
Notes: 2.1.3.2 Configuring Login Enhancement Features

## Slide 19: Enable Login Enhancements
Command Syntax: login block-for
Example: login quiet-mode access-class
Example: login delay
Notes: 2.1.3.3 Enable Login Enhancements
Syntax Checker: Configure Enhanced Login Security on R2

## Slide 20: Logging Failed Attempts
Generate Login Syslog Messages
Example: show login failures
Notes: 2.1.3.4 Logging Failed Attempts

## Slide 21: Topic 2.1.4: Configuring SSH

## Slide 22: Steps for Configuring SSH
Example SSH Configuration
Example Verification of SSH
Notes: 2.1.4.1 Steps for Configuring SSH

## Slide 23: Modifying the SSH Configuration
Notes: 2.1.4.2 Modifying the SSH Configuration
Syntax Checker: Enable SSH on R2

## Slide 24: Connecting to an SSH-Enabled Router
Two ways to connect:
Enable SSH and use a Cisco router as an SSH server or SSH client.
  As a server, the router can accept SSH client connections
  As a client, the router can connect via SSH to another SSH-enabled router
Use an SSH client running on a host, such as PuTTY, OpenSSH, or TeraTerm.
Notes: 2.1.4.3 Connecting to an SSH-Enabled Router

## Slide 25: Section 2.2: Assigning Administrative Roles
Upon completion of this section, you should be able to:
Configure administrative privilege levels to control command availability.
Configure role-based CLI access to control command availability.

## Slide 26: Topic 2.2.1: Configuring Privilege Levels

## Slide 27: Limiting Command Availability
Levels of access commands:
User EXEC mode (privilege level 1)
  Lowest EXEC mode user privileges
  Only user-level command available at the router> prompt
Privileged EXEC mode (privilege level 15)
  All enable-level commands at the router# prompt
Privilege levels:
Level 0: Predefined for user-level access privileges.
Level 1: Default level for login with the router prompt.
Level 2-14: May be customized for user-level privileges.
Level 15: Reserved for the enable mode privileges.
Privilege Level Syntax
Notes: 2.2.1.1 Limiting Command Availability

## Slide 28: Configuring and Assigning Privilege Levels
Notes: 2.2.1.2 Configuring and Assigning Privilege Levels

## Slide 29: Limitations of Privilege Levels
No access control to specific interfaces, ports, logical interfaces, and slots on a router
Commands available at lower privilege levels are always executable at higher privilege levels
Commands specifically set at higher privilege levels are not available for lower privilege users
Assigning a command with multiple keywords allows access to all commands that use those
Notes: 2.2.1.3 Limitations of Privilege Levels
Syntax Checker: Configure Privilege Levels on R2

## Slide 30: Topic 2.2.2: Configuring Role-Based CLI

## Slide 31: Role-Based CLI Access
For example:
Security operator privileges
  Configure AAA
  Issue show commands
  Configure firewall
  Configure IDS/IPS
  Configure NetFlow
WAN engineer privileges
  Configure routing
  Configure interfaces
  Issue show commands
Notes: 2.2.2.1 Role-Based CLI Access

## Slide 32: Role-Based Views
Notes: 2.2.2.2 Role-Based Views

## Slide 33: Configuring Role-Based Views
Step 1
Step 2
Step 3
Step 4
Notes: 2.2.2.3 Configuring Role-Based Views
Syntax Checker: Configure Views on R2

## Slide 34: Configuring Role-Based CLI Superviews
Step 1
Step 2
Step 3
Notes: 2.2.2.4 Configuring Role-Based CLI Superviews
Syntax Checker: Configure Superviews on R2

## Slide 35: Verify Role-Based CLI Views
Enable Root View and Verify All Views
Notes: 2.2.2.5 Verify Role-Based CLI Views

## Slide 36: Section 2.3: Monitoring and Managing Devices
Upon completion of this section, you should be able to:
Use the Cisco IOS resilient configuration feature to secure the Cisco IOS image and configuration files.
Compare in-band and out-of band management access.
Configure syslog to log system events.
Configure secure SNMPv3 access using ACL
Configure NTP to enable accurate timestamping between all devices.

## Slide 37: Topic 2.3.1: Securing Cisco IOS Image and Configuration Files

## Slide 38: Cisco IOS Resilient Configuration Feature
Notes: 2.3.1.1 Cisco IOS Resilient Configuration Feature

## Slide 39: Enabling the IOS Image Resilience Feature
Notes: 2.3.1.2 Enabling the IOS Image Resilience Feature

## Slide 40: The Primary Bootset Image
Notes: 2.3.1.3 The Primary Bootset Image

## Slide 41: Configuring Secure Copy
Configure the router for server-side SCP with local AAA:
Configure SSH
Configure at least one user with privilege level 15
Enable AAA
Specify that the local database is to be used for authentication
Configure command authorization
Enable SCP server-side functionality
Notes: 2.3.1.4 Configuring Secure Copy

## Slide 42: Recovering a Router Password
Connect to the console port.
Record the configuration register setting.
Power cycle the router.
Issue the break sequence.
Change the default configuration register with the confreg 0x2142 command.
Reboot the router.
Press Ctrl-C to skip the initial setup procedure.
Put the router into privileged EXEC mode.
Copy the startup configuration to the running configuration.
Verify the configuration.
Change the enable secret password.
Enable all interfaces.
Change the config-register with the config-register configuration_register_setting.
Save the configuration changes.
Notes: 2.3.1.5 Recovering a Router Password

## Slide 43: Password Recovery
Password Recovery Functionality is Disabled
No Service Password Recovery
Disable Password Recovery
Notes: 2.3.1.6 Password Recovery

## Slide 44: Topic 2.3.2: Secure Management and Reporting

## Slide 45: Determining the Type of Management Access
In-Band Management:
Apply only to devices that need to be managed or monitored
Use IPsec, SSH, or SSL when possible
Decide whether the management channel need to be open at all time
Out-of-Band (OOB) Management:
Provide highest level of security
Mitigate the risk of passing management protocols over the production network
Notes: 2.3.2.1 Determining the Type of Management Access
2.3.2.2 Out-of-Band and In-Band Access

## Slide 46: Topic 2.3.3: Using Syslog for Network Security

## Slide 47: Introduction to Syslog
Notes: 2.3.3.1 Introduction to Syslog

## Slide 48: Syslog Operation
Notes: 2.3.3.2 Syslog Operation

## Slide 49: Syslog Message
Security Levels
Example Severity Levels
Notes: 2.3.3.3 Syslog Message

## Slide 50: Syslog Message (Cont.)
Notes: 2.3.3.3 Syslog Message
2.3.3.4 Activity - Parts 1-3 : Interpret Syslog Output

## Slide 51: Syslog Systems
Notes: 2.3.3.5 Syslog Systems

## Slide 52: Configuring System Logging
Step 1
Step 2 (optional)
Step 3
Step 4
Notes: 2.3.3.6 Configuring System Logging

## Slide 53: Topic 2.3.4: Using SNMP for Network Security

## Slide 54: Introduction to SNMP
Notes: 2.3.4.1 Introduction to SNMP

## Slide 55: Management Information Base
Cisco MIB Hierarchy
Notes: 2.3.4.2 Management Information Base

## Slide 56: SNMP Versions
Notes: 2.3.4.3 SNMP Versions

## Slide 57: SNMP Vulnerabilities
Notes: 2.3.4.4 SNMP Vulnerabilities

## Slide 58: SNMPv3
Message integrity & authentication
Encryption
Access control
Transmissions from manager to agent may be authenticated to guarantee the identity of the sender and the integrity and timeliness of a message.
SNMPv3 messages may be encrypted to ensure privacy.
Agent may enforce access control to restrict each principal to certain actions on specific portions of data.
Notes: 2.3.4.5 SNMPv3

## Slide 59: Configuring SNMPv3 Security
Notes: 2.3.4.6 Configuring SNMPv3 Security

## Slide 60: Secure SNMPv3 Configuration Example
Notes: 2.3.4.7 Secure SNMPv3 Configuration Example
Syntax Checker: Configure SNMPv3 Authentication Using an ACL

## Slide 61: Verifying the SNMPv3 Configuration
Notes: 2.3.4.8 Verifying the SNMPv3 Configuration

## Slide 62: Topic 2.3.5: Using NTP

## Slide 63: Network Time Protocol
Notes: 2.3.5.1 Network Time Protocol

## Slide 64: NTP Server
Sample NTP Topology
Sample NTP Configuration on R1
Sample NTP Configuration on R2
Notes: 2.3.5.2 NTP Server

## Slide 65: NTP Authentication
Notes: 2.3.5.3 NTP Authentication
Syntax Checker: Configure NTP Authentication on R1

## Slide 66: Section 2.4: Using Automated Security Features
Upon completion of this section, you should be able to:
Use security audit tools to determine IOS-based router vulnerabilities.
Use AutoSecure to enable security on IOS-based routers.

## Slide 67: Topic 2.4.1: Performing a Security Audit

## Slide 68: Discovery Protocols CDP and LLDP
Notes: 2.4.1.1 Discovery Protocols CDP and LLDP

## Slide 69: Settings for Protocols and Services
There is a detailed list of security settings for protocols and services provided in Figure 2 of this page in the course.
Additional recommended practices to ensure a device is secure:
Disable unnecessary services and interfaces.
Disable and restrict commonly configured management services.
Disable probes and scans. Ensure terminal access security.
Disable gratuitous and proxy ARPs
Disable IP-directed broadcasts.
Notes: 2.4.1.2 Settings for Protocols and Services

## Slide 70: Topic 2.4.2: Locking Down a Router Using AutoSecure

## Slide 71: Cisco AutoSecure
Notes: 2.4.2.1 Cisco AutoSecure

## Slide 72: Using the Cisco AutoSecure Feature
Notes: 2.4.2.2 Using the Cisco AutoSecure Feature

## Slide 73: Using the auto secure Command
The auto secure command is entered
Wizard gathers information about the outside interfaces
AutoSecure secures the management plane by disabling unnecessary services
AutoSecure prompts for a banner
AutoSecure prompts for passwords and enables password and login features
Interfaces are secured
Forwarding plane is secured
Notes: 2.4.2.3 Using the auto secure Command
Syntax Checker: Use AutoSecure to Secure R1

## Slide 74: Section 2.5: Securing the Control Plane
Upon completion of this section, you should be able to:
Configure a routing protocol authentication.
Explain the function of Control Plane Policing.

## Slide 75: Topic 2.5.1: Routing Protocol Authentication

## Slide 76: Routing Protocol Spoofing
Consequences of protocol spoofing:
Redirect traffic to create routing loops.
Redirect traffic so it can be monitored on an insecure link.
Redirect traffic to discard it.
Notes: 2.5.1.1 Routing Protocol Spoofing

## Slide 77: OSPF MD5 Routing Protocol Authentication
Notes: 2.5.1.2 OSPF MD5 Routing Protocol Authentication

## Slide 78: OSPF SHA Routing Protocol Authentication
Notes: 2.5.1.3 OSPF SHA Routing Protocol Authentication
Syntax Checker: Configure OSPF Authentication Using SHA 256

## Slide 79: Topic 2.5.2: Control Plane Policing

## Slide 80: Network Device Operations
Notes: 2.5.2.1 Network Device Operations

## Slide 81: Control and Management Plane Vulnerabilities
Notes: 2.5.2.2 Control and Management Plane Vulnerabilities

## Slide 82: CoPP Operation
Notes: 2.5.2.3 CoPP Operation
2.5.2.4 Activity - Identify the Features of CoPP
2.5.2.5 Activity - Identify the Network Device Security Features

## Slide 83: Section 2.6: Summary
Chapter Objectives:
Configure secure administrative access.
Configure command authorization using privilege levels and role-based CLI.
Implement the secure management and monitoring of network devices.
Use automated features to enable security on IOS-based routers.
Implement control plane security.
Notes: 2.6.1.1 Packet Tracer - Configure Cisco Routers for Syslog, NTP, and SSH Operations

## Slide 85: Instructor Resources
Remember, there are helpful tutorials and user guides available via your NetSpace home page. (https://www.netacad.com)
These resources cover a variety of topics including navigation, assessments, and assignments.
A screenshot has been provided here highlighting the tutorials related to activating exams, managing assessments, and creating quizzes.
1
2
Notes: https://www.netacad.com